## Slide 1: Universal Robots
Advanced Training

## Slide 2: Welcome to Advanced Training
A practical hands-on experience
USB stick with simulator
30 min. multi-choice examination at end of training

## Slide 3: Presenting the Trainer
Name: <Name>
Role: <Job description>

## Slide 4
1
URScript
2
Variables
3
Features
4
Advanced use of TCP
5
Modbus Server
6
FTP Server
7
Dashboard Server
8
Client Interfaces
9
Socket Communication
10
Program Troubleshooting

## Slide 5
1
UR Script
2
Variables
3
Features
4
Advanced use of TCP
5
Modbus Server
6
FTP Server
7
Dashboard Server
8
Client Interfaces
9
Socket Communication
10
Program Troubleshooting
1
URScript

## Slide 6
URScript
1
What is URScript?
URScript
  High level script language developed by UR
  Can be used instead of building program structure in the Polyscope GUI
  Similarities to Python script language
  Script manual contains definitions of all available script codes
  Polyscope programs are converted to URScript before execution
  A number of potential approaches to using URScript
Notes: What is URScript?
Introduction to script

## Slide 7
URScript
1
How to use URScript
There are a number of ways to use URScript
  Assignment
  Script Code – Line
  Script Code – File
  Calling functions
  Client Interfaces
Notes: How to use URScript
Explain the different options of using script

## Slide 8
URScript
1
Assignment
Executes script command
Assigns returned value to a variable.
Allows values returned to be viewed in variables window.
Notes: Assignment

## Slide 9
URScript
1
Expression Editor
Most common script codes listed
Saves having to type out whole commands
Sample program using force()
Robot Program MoveL Waypoint_1 IF force() < 30 Waypoint_2
Notes: Expression editor
Create sample program:
1. Insert vertical linear movement between two waypoints.
2. Reduce speed to 100 mm.
3. Move the bottom waypoint inside of an IF-command
4. Define condition in IF to be force() < 30 :it might be required to adjust the value
5. IMPORTANT: Make sure to check the box ”Check expression continuously”
Demonstrate how it is possible to stop the downward movement by hand.
Show the variable tab and verify the force value changes while running the program

## Slide 10
URScript
1
Script Code - Line
Execute a single line of URScript
  Variables defined in script do not appear in Variables window
  Waypoints in script do not appear in Graphics window
Robot Program movel(p[0,-0.4,0.3,0,3.14,0]) sleep(1) movel(p[0.2,-0.4,0.3,0,3.14,0])
Notes: Script code – line
Make sample with three script lines

## Slide 11
URScript
1
Script Code - File
Load and run an existing script file
Execute multiple lines of script
File transfer over ethernet covered later in training session
Select Edit-button
Notes: Script code – file
Create and save new script file

## Slide 12
URScript
1
Script Code – Open file
Select Open button to open an existing .script file
Notes: Script code – file
Create and save new script file

## Slide 13
URScript
1
Script Code - Open file
The Filter will automatically show all .script file.
Older version may not, so you have you select All in Filter
Select Open when finished
Notes: Script code – file
Create and save new script file

## Slide 14
URScript
1
Script Code – Create new file
Insert three new lines
Write script code for each line
Save & Exit
Notes: Script code – file
Create and save new script file

## Slide 15
URScript
1
Script Code - File
Run program
Notes: Script code – file
Create and save new script file

## Slide 16
A function in script is declared as
  def name()
    script
    …
  end
A function can take argument and return processed argument
  def name(argument)
    …
    …
    return
  end
A function can be called multiple times within a program
URScript
1
Script Code - Functions
Notes: Script code – Functions

## Slide 17
URScript
1
Script Code - Functions
Function that adds two values and returns result
  Create script file with function
    Give function a name
    Define two arguments
    Insert return
Declare two variables with operator input
Declare variable and assign the function incl. arguments
Notes: Script code – Functions
Demonstrate how to call a function.
In this case, a simple calculator

## Slide 18
URScript
1
Client Interfaces
Script codes can be sent directly to the controller over Ethernet from an external machine
3 client interfaces running automatically at boot
Explained later in client interfaces section
Notes: Client interfaces

## Slide 19
URScript
1
Lab Exercise
Write a short URScript file that:
  Defines a function
  Receives an argument
  Processes the received value
  Returns the processed value
Load this file into a program
Call function from assignment
Execute program
View results
Notes: URScript Lab Exercise

## Slide 20
1
UR Script
2
Variables
3
Features
4
Advanced use of TCP
5
Modbus Server
6
FTP Server
7
Dashboard Server
8
Client Interfaces
9
Socket Communication
10
Program Troubleshooting
2
Variables

## Slide 21
Variables
2
What is a Variable
Variable is a storage location (container)
  Content of container can change
Variables are read and write
  Value can be overwritten
  Value can be read
  Variable can be compared with other variable or sensor state
Core Training
Wrap-up
Notes: What is a variable?
A variable is a storage location (container).
Content (value) of the container can change.
Variables (in PolyScope) are read and write:
» Value can be overwritten by the program
» Value can be read and compared with another variable or sensor state

## Slide 22
Variables
2
Variable Types
Core Training
Wrap-up
boolean | true/false
integer | whole number (32 bit)
floating point | real number (decimal)
string | text (ASCII characters)
pose | position variable p[x,y,z,rx,ry,rz]
list | array of variables
var type | value
Notes: Variable type
PolyScope can use a range of different variable types
» boolean
» integer
» floating point
» string
» pose
» list (contains a list of other variables)
EXAMPLE:
» A variable of boolean type can contain either True or False

## Slide 23
Variables
2
Variable Types
Core Training
Wrap-up
local | program
global | installation
scope | location
Local variables
  Declared in program
  Accessible from same program
  Value cleared at power down
Global variables
  Declared in Installation
  Accessible from programs using same Installation
  Value stored in file on disk
Notes: Variable scope
PolyScope distinguishes between:
» Local variables
» Global variables

## Slide 24
Variables
2
How to insert a variable
Assignment command
  Define variable name
  Declare variable type
  Assign value to variable
Robot Program var_1 = True Wait 0.5 var_1 = False Wait 0.5
Core Training
Wrap-up
Notes: How to insert variable
Make sample program where a local boolean variable changes state every 500 ms
Save program as var_bool.urp

## Slide 25
Variables
2
Pose Variable
Definition
  A vector describing the location and orientation in Cartesian space.
  Combination of
    position vector (x,y,z)
    rotation vector (rx,ry,rz)
  Units
    x,y,z = meters
    rx,ry,rz = radians
    pose_var = p[ x , y , z , rx , ry , rz ]
variable name
TCP position
rotation vector
Notes: Pose variable
Explain the definition of pose variable
No theoretical limit to the amount of variables available, but system might have slower respons if +50 pose variables are used

## Slide 26
Variables
2
Working with pose Variables
Manual input of pose
  Insert Assignment
  Define variable name
  Enter expression as pose e.g.:
    x = 100 mm
    y = -400 mm
    z = 300 mm
    rx = 0
    ry = 3.14
    rz = 0
Notes: Working with pose variables
All pose variables will be listed in dropdown box, both Installation and Program variables.

## Slide 27
Variables
2
Working with pose Variables
Move to pose
  Insert Move
  Select variable position
  Use variable
  NOTE: If first waypoint in program is variable or relative, the AutoMove function will be skipped
Notes: Working with pose variables
All pose variables will be listed in dropdown box, both Installation and Program variables.

## Slide 28
A number of script functions for pose variables are available
Variables
2
Script functions for pose variables
get_actual_tcp_pose() | Returns the current measured TCP pose
get_actual_tcp_speed() | Returns the current measured TCP speed
get_inverse_kin() | Inverse kinematics
get_target_tcp_pose() | Returns the current target TCP pose
get_target_tcp_speed() | Returns the current target TCP speed
interpolate_pose(p_from, p_to, alpha) | Linear interpolation of tool position and orientation
pose_add(p_1, p_2) | Pose addition
pose_dist(p_from, p_to) | Returns distance between two poses
pose_inv(p_from) | Get the inverse of a pose
pose_sub(p_to, p_from) | Pose subtraction
pose_trans(p_from, p_to) | Pose transformation
Script code | Function
Notes: Scrip functions for pose variables
Three script codes will be explained in the following slides:
get_actual_tcp_pose()
pose_add()
pose_trans()

## Slide 29
How to read current position and move up to safe position
  Add BeforeStartSequence
  Read current position, save in variable
  Save z-value in other variable
  Define new pose variable
    Same pose as current except z-value
    Set z-value to 400 mm.
  Move to safe_pos variable
    Reduce speed
Variables
2
Example: get_actual_tcp_pose()
BeforeStartSequence cp = get_actual_tcp_pose() z = cp[2] safe_pos = p[cp[0], cp[1], 0.4, cp[3], cp[4], cp[5]] Wait 1 MoveL safe_pos Robot Program Halt
x | [0]
y | [1]
z | [2]
rx | [3]
ry | [4]
rz | [5]
Pose designations | 
p[x,y,z,rx,ry,rz] | index no.
Notes: get_actual_tcp_pose()
Function reads the Cartesian position as seen in Move-tab (select Base as Feature)
Save as get_actual_tcp_pose.urp

## Slide 30
Variables
2
Example: pose_add()
How to move from reference position to variable pick position
  Simulate data from vision
  e.g. object is offset from refpoint:
    x = 250 mm
    y = 120 mm
    rz = 31 degrees
  Define pose variable containing the offsets
  Add variable to refpoint using pose_add()
    pose_add() uses Base as reference
Robot Program MoveJ refpoint Wait DI[0] = True Calc-folder x = 250 y = 120 rz = 31 offset = p[(x/1000),(y/1000),0,0,0,d2r(rz)] pick_pos = pose_add(refpoint, offset) MoveL pick_pos
refpoint
BASE
X
Y
RZ
Y
X
BASE feature as reference
Notes: pose_add()
Adds two poses together, uses Base as reference
Save as pose_add.urp

## Slide 31
Variables
2
Example: pose_trans()
In a real application it is very unlikely that the vision frame will be aligned with the base frame
If we use pose_add() here, it will be very difficult to reach the correct target
We need to transform our X and Y into the target frame
This is where pose_trans() comes in.
Base Feature as reference
RZ
refpoint
BASE
Y
X
X
Y
Notes: pose_trans()
Transforms first pose in expression using second pose as reference
Save as pose_trans.urp
TIP: Refpoint can be replaced with a user-defined Feature, then this Feature becomes reference

## Slide 32
Variables
2
Example: pose_trans()
How to move from reference position to variable pick position
  Simulate data from vision
  e.g. object is offset from refpoint:
    x = 250 mm
    y = 120 mm
    rz = 31 degrees
  Define pose variable containing the offsets
  Add variable to refpoint using pose_trans()
    pose_trans() uses first pose as reference
Refpoint as reference
X
Y
RZ
refpoint
Robot Program MoveJ refpoint Wait DI[0] = True Calc-folder x = 250 y = 120 rz = 31 offset = p[(x/1000),(y/1000),0,0,0,d2r(rz)] pick_pos = pose_trans(refpoint, offset) MoveL pick_pos
BASE
Y
X
Notes: pose_trans()
Transforms first pose in expression using second pose as reference
Save as pose_trans.urp
TIP: Refpoint can be replaced with a user-defined Feature, then this Feature becomes reference

## Slide 33
Variables
2
Lab Exercise part 1
Starting from the robot’s current position, create a square trajectory with 10cm sides:
Use:
  get_actual_tcp_pose()
  pose_trans()
  MoveL
create a square with
Use variable x to define side length
x
x
a
b
c
d
Notes: Variables Lab Exercise

## Slide 34
Variables
2
Lab Exercise part 2
Take program from exercise part 1, using same variables
Move around the square 3 times
Add 5cm to the side length each time
10cm
15cm
20cm
Notes: Variables Lab Exercise

## Slide 35
1
UR Script
2
Variables
3
Features
4
Advanced use of TCP
5
Modbus Server
6
FTP Server
7
Dashboard Server
8
Client Interfaces
9
Socket Communication
10
Program Troubleshooting
3
Features

## Slide 36
Feature is a Cartesian coordinate system
  A coordinate system defines a plane or space by axes from a fixed point called the origin
  Feature is saved as a pose variable
Features
3
What is a Feature
Y
X
Z
RZ
RX
RY
origin
Notes: What is a Feature?

## Slide 37
Robot operates relative to features
  Base feature
  Tool feature
Tool position
  X, Y, Z = position of TCP
    Unit: mm / inch
  Rx, Ry, Rz = orientation
    Unit: radians
  NOTE: Orientation is given as a rotation vector, where the length of the vector is the angle to be rotated in degrees
Features
3
What is a Feature
Notes: What is a feature?
The rotation is not in Euler angles.
They are defined as a rotation vector.
The three values are the X-Y-Z values of the vector and the Euclidean norm is the rotation around this vector in radians.

## Slide 38
  Located at the base of the robot
  Origin in centre of base
Features
3
Base feature
Y
X
Z
RZ
RX
RY
Notes: Base feature
Base coordinate system = also known as World Coordinates in other robot programming languages

## Slide 39
  Origin in centre of tool flange
Features
3
Tool feature
Y
X
Z
RZ
RX
RY
Notes: Tool feature
Tool feature is dynamic, as it always has its origin in center of TCP

## Slide 40
  Origin in centre of TCP
Features
3
Tool feature
Y
X
Z
RZ
RX
RY
Notes: Tool feature
When TCP is defined, origin of the Tool feature will be in center of TCP

## Slide 41
  Defined by the operator
Features
3
User defined feature
X
Z
RZ
RZ
RY
Y

## Slide 42
Features
3
Setup Feature
Features
  In PolyScope a Plane is defined as a Feature
  Multiple Features can be set
  Set Feature as
    Point
    Line
    Plane
Add Feature
  Plane
Notes: Setup feature

## Slide 43
Properties
  Show axes
    Display colors
  Joggable
    Enable feature in Move-tab
  Variable
    Create a copy of the feature
  Move robot here
    Position TCP perpendicular to feature
Features
3
Setup Feature
Notes: Setup feature
Feature is fixed, but if Variable is selected, then a copy of the feature can be modified
Demonstrate how to define a feature as Plane
» Click Plane-button to add new plane
» Use A4 sheet or similar to create feature

## Slide 44
Select Feature
  Jog using arrow keys
  Expression editor
Features
3
Jog relative to Feature
Notes: Jog relative to Feature
Go to MOVE-tab and select the Plane as feature
Demonstrate how to jog relative to the user-defined Feature

## Slide 45
Features
3
Move-command
  Feature applicable to
    MoveL
    MoveP
    MoveC
  Shared parameters
    Select user-defined feature
Jog relative to Feature
Notes: Working with Features
MoveJ waypoints are always with respect to angular positions, so Feature can not be selected

## Slide 46
Features
3
Create program
  Insert MoveJ
    Teach home pose
  Insert MoveL
    Select Plane_1 as Feature
    Teach 4 waypoints
  Run program
  Re-teach Feature
    Check Feature as Variable
    Verify waypoints are shifted
Working with Features
Robot Program MoveJ home MoveL Waypoint_1 Waypoint_2 Waypoint_3 Waypoint_4 Waypoint_1
wp2
wp1
wp3
wp4
home
Plane_1
Plane_1 re-taught
Notes: Working with Features
Demonstrate how to teach waypoints relative to user-defined feature
Then modify the Feature and verify that the entire program is shifted accordingly
Save as feature.urp

## Slide 47
Features
3
Use sample program
  Use script code to offset Feature
    pose_add()
    pose_trans()
  How to
    Define offset in Y
    Use offset in pose var
    Use pose var to offset feature
Working with Features
Robot Program MoveJ home y = 0.05 offset = p[0,y,0,0,0,0] Plane_1_var = pose_trans(Plane_1_var,offset) MoveL Waypoint_1 Waypoint_2 Waypoint_3 Waypoint_4 Waypoint_1
wp2
wp1
wp3
wp4
home
Plane_1
Plane_1 offset
Notes: Offset Feature
Make sample program, where the offset is accumulated for every cycle
Save as offset_feature.urp

## Slide 48
Use sample program
  Create two Features
    Plane_1
    Plane_2
  Use two inputs to switch Feature
    If DI[0] is high, use Plane_1
    If DI[1] is high, use Plane_2
Features
3
Working with Features
Robot Program MoveJ home IF DI[0] = True Plane_1_var = Plane_1 ELSEIF DI[1] = True Plane_1_var = Plane_2 MoveL Waypoint_1 Waypoint_2 Waypoint_3 Waypoint_4 Waypoint_1
wp2
wp1
wp3
wp4
home
Plane_1
Plane_2
Notes: Switch between multiple Features
Make sample program, where the offset is accumulated for every cycle
Save as switch_between_features.urp

## Slide 49
Create two feature planes:
  Plane_1
  Plane_2
Set them as variable
Save Installation
Lab Exercise part 1
Features
3
Plane_1
Plane_2
Notes: Features Lab Exercise

## Slide 50
Create a program:
  Add a MoveL
  Set feature in MoveL as Plane_1
  Add 4 waypoints to MoveL
  Set first waypoint at origin of Plane_1
Features
3
Lab Exercise part 2
wp4
wp3
wp2
wp1
Notes: Features Lab Exercise

## Slide 51
Features
3
Once the MoveL is complete
  Offset plane_1 +10cm in y direction
  Repeat MoveL
  Offset another 10cm in same direction
  Repeat MoveL
Lab Exercise part 3
wp4
wp3
wp2
wp1
wp4
wp3
wp2
wp1
wp4
wp3
wp2
wp1
Offset 1
Offset 2
Notes: Features Lab Exercise

## Slide 52
After the third MoveL has been completed
  Set plane_1_var to the second feature (plane_2)
  Execute the movements in the plane_2 feature frame.
Features
3
Lab Exercise part 4
wp4
wp3
wp2
wp1
wp4
wp3
wp2
wp1
wp4
wp3
wp2
wp1
Plane_1_Var = Plane_1
Offset 2
wp4
wp3
wp2
wp1
wp4
wp3
wp2
wp1
wp4
wp3
wp2
wp1
Plane_1_Var = Plane_2
Switch to Feature 2
Notes: Features Lab Exercise

## Slide 53
1
UR Script
2
Variables
3
Features
4
Advanced use of TCP
5
Modbus Server
6
FTP Server
7
Dashboard Server
8
Client Interfaces
9
Socket Communication
10
Program Troubleshooting
4
Advanced use of TCP

## Slide 54
Definition:
  Centre of gravity is the location where tool payload is balanced
Script code
  set_payload(m, CoG)
    m = mass in kilogram
    CoG = Center of Gravity (CoGx, CoGy, CoGz) in meters
NOTE:
  If CoG is not defined, software will use TCP as CoG.
Advanced use of TCP Features
4
Centre of Gravity (CoG)
TCP
CoG
Notes: Center of Gravity (CoG)
  = centerpoint of tool weight
Tip: demonstrate CoG with a pen on your fingertip.
If pen stays horizontal, you have demonstrated CoG of pen

## Slide 55
GUI TCP Payload settings
  Easiest way to define CoG
  (see next slide)
Still need to use script code if CoG changes a lot during execution.
Advanced use of TCP Features
4
Centre of Gravity (CoG)
Notes: Center of Gravity (CoG)
  = centerpoint of tool weight
Tip: demonstrate CoG with a pen on your fingertip.
If pen stays horizontal, you have demonstrated CoG of pen

## Slide 56
The TCP position can be determined by moving the tool tip to the same position from 3 different angles
Once you have taught these positions the TCP x,y,z values will be calculated
Adding a fourth pose improves accuracy
Advanced use of TCP Features
4
Teaching TCP Position
Notes: Center of Gravity (CoG)
  = centerpoint of tool weight
Tip: demonstrate CoG with a pen on your fingertip.
If pen stays horizontal, you have demonstrated CoG of pen

## Slide 57
Click Position button to Teach TCP Position
Set 3 or 4 points
Indicator LED will show status of TCP calculation and quality of each point
Advanced use of TCP Features
4
Teaching TCP Position
Notes: Tool feature
When TCP is defined, origin of the Tool feature will be in center of TCP

## Slide 58
Setup TCP
  In Installation-tab only one TCP can be setup.
  Script code can be used for setting up multiple TCP’s
Script code
  set_tcp(pose)
  pose = p[x,y,z,rx,ry,rz]
Installation
  Set Base feature as variable
NOTE:
  Only MoveL and MoveP will be affected by set_tcp()
Advanced use of TCP Features
4
Multiple TCP
tcp2 = p[x2,0,z2,0,ry2,0]
z1
x1
z2
x2
ry2
tcp1 = p[x1,0,z1,0,0,0]
Notes: Multiple TCP
How to use more than one TCP in same program.
It is assumed that tool is rotated only around Y-direction of Tool feature

## Slide 59
Advanced use of TCP Features
4
Setup tcp1
    x1 = 150 mm.
    z1 = 150 mm.
  tcp1 = p[0.15, 0, 0.15, 0, 0, 0]
Setup tcp2
    x2 = -200 mm.
    z2 = 140 mm.
    ry2 = -25 °
  tcp2 = p[-0.2, 0, 0.14, 0, d2r(-25), 0]
Multiple TCP
tcp2 = p[x2,0,z2,0,ry2,0]
z1 = 150
x1 = 150
z2 = 140
x2 = -200
zy2 = -25°
tcp1 = p[x1,0,z1,0,0,0]
Notes: Multiple TCP
Use script code d2r() for converting -25 degrees to radians

## Slide 60
Set TCP_1 as default
TCP_1
    x1 = 150 mm.
    z1 = 150 mm.
Advanced use of TCP Features
4
Setting TCP
Notes: Multiple TCP
Use script code d2r() for converting -25 degrees to radians

## Slide 61
Advanced use of TCP Features
4
Setting TCP
Click New to add second TCP
TCP_2
  x2 = -200 mm.
  z2 = 140 mm.
  ry2 = -25 °
Rotation must be specified in Radians
  25*pi/180 = 0.4363
Notes: Multiple TCP
Use script code d2r() for converting -25 degrees to radians

## Slide 62
Advanced use of TCP Features
4
Implement in program
Sample program
  Set Base feature as variable in Installation-tab
  Declare integer variable tcp for switching between multiple tcp’s
  Set feature as Base in MoveL-command
BeforeStartSequence tcp = 1 tcp1 = p[0.15,0,0.15,0,0,0] tcp2 = p[-0.2,0,0.14,0,d2r(-25),0] MoveJ home Robot Program IF tcp = 1 set_tcp(tcp1) tcp = 2 ELSEIF tcp = 2 set_tcp(tcp2) tcp = 1 MoveL Waypoint_1 Waypoint_2 Waypoint_1
Notes: Implement in program
It is important to set Base feature as variable and use Base as feature in MoveL-command

## Slide 63
Simulate an installation with two tools, one gripper and a screwdriver
Gripper (tcp1)
  Z Offset 20cm
Screwdriver (tcp2)
  X offset 20cm
  Z offset 5cm
  RY offset 90°
NOTE:
  Only MoveL, MoveP and MoveC will be affected by set_tcp()
Advanced use of TCP Features
4
Lab Exercise part 1
tcp1 = p[0,0,z1,0,0,0]
z2
x2
z1
ry2
tcp2 = p[x2,0,z2,0,d2r(ry2),0]
Notes: Advanced use of TCP Lab Exercise

## Slide 64
Advanced use of TCP Features
Simulate picking then placing a square work piece with gripper, then screwing it in 4 locations.
Set TCP Gripper (tcp1)
  Move to a pick point of your choice
  Move to a place point of your choice
Set TCP Screwdriver (tcp2)
  Use pose_trans() to define 4 fixing points at
  x=±7.5cm and y=±7.5cm from place point
Write a subprogram
  MoveL to relative waypoint Z+5cm in tool frame
  MoveL to relative waypoint Z+5cm in tool frame
  Call after every waypoint in main program
4
Lab Exercise part 2
Notes: Advanced use of TCP Lab Exercise

## Slide 65
1
UR Script
2
Variables
3
Features
4
Advanced use of TCP
5
Modbus Server
6
FTP Server
7
Dashboard Server
8
Client Interfaces
9
Socket Communication
10
Program Troubleshooting
5
Modbus Server

## Slide 66
Modbus Server
Before any TCP/IP based communication, PC and robot network must be configured.
Under network device properties setup:
  IP address
  Subnet mask
IP-address on robot and PC should be the same part from the last number. In this case:
  192.16.17.x
Both Subnet masks should be
  255.255.255.0
5
PC Network Configuration
Notes: PC Network Configuration

## Slide 67
Go to Setup Robot, select Setup Network and setup:
  IP-address
  Subnet mask
IP address should be in the same format as PC:
  192.16.17.x
Subnet mask should be
  255.255.255.0
Modbus Server
5
Robot Network Configuration
Notes: Robot Network Configuration

## Slide 68
Modbus TCP
  Ethernet based communication protocol
Communication protocol
  A protocol is a common language with which two devices can communicate
  Possible to transfer data between devices
  Client / Server relationship
Modbus Server
5
What is TCP modbus
Ethernet
Device 2
Device 1
Core Training
Wrap-up
Notes: What is Modbus TCP?
Ethernet based communication protocol
- A communication protocol is a common language with which two devices can communicate.
- Used for data transfer between devices.

## Slide 69
Server
  One device acts as Server
  Listening on requests from Client
Client
  Other device(s) acts as Client
  Sends requests to Server
  Each device must have a unique IP-address
Modbus Server
5
Client / Server
Modbus client
Modbus server
Device 2
Device 1
Core Training
Wrap-up
Notes: Client / Server
Client/Server is sometimes referred to as Master/Slave
Client = Master
Server = Slave

## Slide 70
Available data types for Modbus TCP
Address range
  Each digital signal and register have a unique address
  Address is always specified in documentation provided by vendor
Modbus Server
5
Data Types
Digital inputs | On/Off | Consult documentation provided by vendor of Server device
Digital outputs | On/Off | 
Register inputs | 16 bit | 
Register outputs | 16 bit | 
data type | value | address range
Core Training
Wrap-up
Notes: Data types
Available data types

## Slide 71
Core Training
  Covered how to use robot as Client and connect to a Server
Advanced Training
  Will cover how to use the UR Controller as a Server and accept Client connections
Modbus Server
5
UR Modbus Server
Modbus client
Modbus servers
Ethernet
Notes: UR Modbus Server

## Slide 72
Modbus Server is always running on UR Controller
  IP Address: Set in robot setup menu
  Port no: 502 (no setting needed)
Features:
  Modbus Server transmits information about robot state including:
    Joint Angle/Velocity/Current/Temperature
    TCP Position/Velocity/Offset
    Program state – Emergency stopped/ teach mode etc.
  I/O can be remotely read/written
    I/O state transmitted
    Outputs can be controlled from remote device
  General purpose registers
    128 registers available
Full list of register addresses available on support site
Modbus Server
5
Modbus Server Features
Notes: Modbus Server features
Explain the options for accessing data on the robot

## Slide 73
Access robots own Server
  IP-address: 127.0.0.1
Read TCP position
  Register addresses:
    400 TCP-x in tenth of mm
    401 TCP-y in tenth of mm
    402 TCP-z in tenth of mm
    403 TCP-rx in mrad
    404 TCP-ry in mrad
    405 TCP-rz in mrad
  = in Base frame
  263 isTeachButtonPressed
Modbus Server
5
Access robot Own server
Notes: Access robots own Server
Setup and read current TCP position while jogging robot manually

## Slide 74
Setup register with digital outputs
  Register address = 1
Feature
  Allows manipulation of multiple I/O channels in single operation saving processing time.
Format:
  16 bit integer registers
  [BBBBBBBBTTxxxxxx] B=box , T=tool, x=undef
Modbus Server
5
Access I/O registers
Notes: Access I/O registers

## Slide 75
Modbus Server
5
Modbus Applications
Potential applications for Modbus Server include:
  Controlling the robot IO from a remote device
How to test
  Install Ananas
    Freeware program for testing Modbus functionality
  Setup Ananas as Modbus client
  Switch digital IO in the controller by checking/unchecking bits or edit integer value
Notes: Modbus Applications
Use Ananas for remote connection from laptop to controller

## Slide 76
Modbus Server
5
Write a program to:
  Read digital output register
  Convert to binary list
  Toggle output channel 3
  Convert back to integer
  Write back to register
Run program and watch output change
Lab Exercise 1
Notes: Modbus Server Lab Exercise 1

## Slide 77
Modbus Server
5
Write a program to receive simulated vision coordinates from Modbus server, then move to received position:
  Retrieve pick position variables from Modbus Server general purpose registers
  Move to position, based on pose_trans() example from Variables section.
Register addresses:
  128: new data available (0=no, 255=yes)
  129: x
  130: y
  131: rz
Lab Exercise 2
Refpoint as reference
BASE
Y
X
X
Y
RZ
refpoint
Notes: Modbus Server Lab Exercise 2

## Slide 78
1
UR Script
2
Variables
3
Features
4
Advanced use of TCP
5
Modbus Server
6
FTP Server
7
Dashboard Server
8
Client Interfaces
9
Socket Communication
10
Program Troubleshooting
6
FTP Server

## Slide 79
FTP Server
  Client/server protocol for file transfers
  Ethernet based communication
Purpose
  For convenient transfer of program files
  Easy backup
Server on UR controller
  Server is always running on UR controller
  No settings on UR controller needed
FTP Server
6
What is FTP Server?
Ethernet
UR Controller
PC
File transfer
FTP client
FTP server
Notes: What is FTP Server?

## Slide 80
FTP client
FileZilla
  Freeware FTP client
  filezilla-project.org
  Connection via ssh or sftp
How to connect
  Setup FileZilla
    Host: IP-address on robot
    User: root
    Password: easybot
    Port 22
How to transfer
  Drag’n’drop files between PC and /programs folder on controller
  WARNING: File system on controller is not write-protected, so incorrect use can cause malfunction
FTP Server
6
Notes: FTP Server

## Slide 81
FTP Server
6
Lab Exercise
Make backup of all files in /programs folder
Write a simple program in URSim on your own laptop
Copy it to the /programs folder
Run program on robot
Notes: FTP Server Lab Exercise

## Slide 82
1
UR Script
2
Variables
3
Features
4
Advanced use of TCP
5
Modbus Server
6
FTP Server
7
Dashboard Server
8
Client Interfaces
9
Socket Communication
10
Program Troubleshooting
7
Dashboard Server

## Slide 83
Dashboard server
7
The Dashboard Server
  Allows remote control of the robot over port 29999.
  Control operation of the robot, loading/starting programs
  Get feedback about robot state (is program running/loaded)
  Show/close popups
  Set user access level (disable different parts of the GUI)
  Full list of commands is found on support site
What is the Dashboard Server?
Notes: Dashboard Server
Description of Dashboard functionality

## Slide 84
Dashboard server
6
SocketTest
  Freeware program for testing TCP/IP socket communication
  sockettest.sourceforget.net
How to connect
  Setup IP-address on PC and robot
  Open SocketTest
    Select Client-tab
    Insert IP-address of robot
    Insert port no of Dashboard Server (29999)
    Click Connect
SocketTest
Notes: SocketTest

## Slide 85
Dashboard server
6
Control robot operation remotely
  load <program.urp>
  play (starts loaded program)
  stop (stops running program)
  pause (pauses the running program)
  quit (closes connection)
  shutdown (shuts down and turns off the robot and controller)
Dashboard remote operations
Notes: Dashboard remote operations
How to operate robot from remote

## Slide 86
Dashboard server
7
Request robot state
  running (execution state enquiry)
  robotmode (robot mode enquiry)
  Get loaded program (which program is loaded)
  isProgramSaved (Returns the save state of the active program)
  programState (Returns the state of the active program, or STOPPED if no program is loaded)
Dashboard feedback
Notes: Dashboard feedback

## Slide 87
Dashboard server
7
Open and close popups on the GUI
  popup <popup-text> (open a popup)
  close popup (closes the popup)
Dashboard popups
Notes: Dashboard popups

## Slide 88
Dashboard server
7
Control the available options on the welcome screen
  setUserRole <role>
Dashboard User Roles
programmer | ”SETUP Robot” button is disabled, ”Expert Mode” is available (if correct password is supplied)
operator | Only ”RUN Program” and SHUTDOWN Robot” buttons are enabled, ”Expert Mode” cannot be activated
none | All buttons enabled, ”Expert Mode” is available (if correct password is supplied)
locked | All buttons disabled and ”Expert Mode” cannot be activated
User roles (<role>) | Description
Notes: Dashboard User Roles

## Slide 89
Dashboard server
7
Return robot to the welcome screen
Connect to the dashboard server
Load the program you transferred to the robot via FTP
Play the program
Lab Exercise
Notes: Dashboard Lab Exercise

## Slide 90
1
UR Script
2
Variables
3
Features
4
Advanced use of TCP
5
Modbus Server
6
FTP Server
7
Dashboard Server
8
Client Interfaces
9
Socket Communication
10
Program Troubleshooting
8
Client Interfaces

## Slide 91
Client Interfaces
8
What are Client interfaces?
  Servers that are always running on UR controller
Functionality
  Servers continuously sends stream of data about robot state
  Clients can send URScript commands to Servers
    (Servers are always waiting for incoming commands)
What are Client Interfaces?
Ethernet
UR Controller
PC
Data transfer
Client
Server
Notes: What are Client interfaces?

## Slide 92
Client Interfaces
8
Available interfaces
  Real Time Client Interface is faster than Primary/Secondary
Available interfaces
Transmit | Robot State and additional messages | Robot State messages | Robot State messages | Robot State messages
Receive | URScript commands | URScript commands | URScript commands | URScript commands
Port no. | 30001 | 30002 | 30003 | 30004
 | Primary | Secondary | Real Time | Real-Time Data Exchange (RTDE)
Notes: Available interfaces
Primary and Secondary = 10Hz
Real time and RTDE = 125Hz

## Slide 93
Client Interfaces
8
Datastream
  Transmitted data stream contains a large amount of data
  Mainly used for communication between GUI and controller
  Need to write a program to extract required data from received bytes
  More information on support site
  A lot of work to receive data, not always the best option
Transmitted Datastream
Notes: Transmitted Datastream

## Slide 94
Client Interfaces
8
Send to client interface
  Client Interfaces most useful for sending URScript commands from remote machine
  Individual commands executed in order as received
  Send a function and execute later
  Can write a program in script and execute it without using the GUI.
Sending Commands
Notes: Sending commands

## Slide 95
Client Interfaces
8
Open SocketTest
  Select Client
  Set port no. 30001
  Connect
Send sample commands, e.g:
  popup()
  set_digital_out()
  movel()
  speedj()
  Refer to URScript manual for detailed explanation of script codes syntax
Sending Commands
Notes: Sending Commands

## Slide 96
Client Interfaces
8
From SocketTest send commands to the robot (or URSIM) client interfaces to do the following, (consult the URScript manual for the correct syntax):
Move the Robot TCP in the Base frame with the following parameters:
  Z velocity = 0.3 m/s
  X, Y, RX, RY, RZ velocity all = 0 m/s.
  Timeout = 1 second
  Acceleration = 0.5m/s²
Move the Robot TCP in the Tool frame with the following parameters:
  Z = Z + 0.1 m (add 0.1 m to the current TCP Z value)
  Move in Linearly in tool space
  Velocity = 0.2 m/s
  Acceleration = 0.5m/s²
  Hint: You will need to use get_actual_tcp_pose() and pose_trans() within a movel command.
Lab Exercise
Notes: Client interfaces Lab Exercise

## Slide 97
1
UR Script
2
Variables
3
Features
4
Advanced use of TCP
5
Modbus Server
6
FTP Server
7
Dashboard Server
8
Client Interfaces
9
Socket Communication
10
Program Troubleshooting
9
Socket Communication

## Slide 98
Socket Communication
9
Socket communication
  Simple TCP/IP socket communication is highly useful to pass data between robot and other device
  Robot = Client, other device = Server
Functionality
  Server always listens to the socket for a client to make connection request
  Commands to open/close sockets
  Commands to send/receive different data formats
What are Sockets?
Ethernet
UR Controller
PC
Data transfer
Server
Client
Notes: What are Sockets?

## Slide 99
Socket Communication
9
Open SocketTest
  Select Server
  Define IP-address
  Define a port no.
  Start listening
  IP-address should be same as address on PC
Starting Server
Notes: Starting Server

## Slide 100
Socket Communication
9
socket_open(address, port, socket_name)
  address
  port
  socket_name
  If program opens only one socket, a socket name is not required.
Return value
  TRUE if socket opened successfully
  FALSE if failed
Open a Socket
Robot Program socket_open(”172.16.17.10”, 50000)
Notes: Open a Socket

## Slide 101
Socket Communication
9
socket_send_string(str, socket_name)
  str
  socket_name
Return value
  none
Send a string
Robot Program socket_send_string(”test”)
Notes: Send a string

## Slide 102
Socket Communication
9
Start Server
Send string to Server
  Open socket
  Wait until socket is open
  Send string
  Close socket
Verify result on Server
Sample send string
Notes: Sample send string

## Slide 103
Socket Communication
9
Socket_read_ascii_float (n, socket_name)
  number
  socket_name
Return value
  list of floats + 1 integer
  (first number in list is integer and defines amount of valid floats in list)
Receive a response
Robot Program socket_read_ascii_float(3)
Notes: Receive a response

## Slide 104
Continue sample
  Open socket
  Wait until socket is open
  Send string
  Send request to Server
  Read three floats
  Wait until three floats received
  Save floats in variables *
    x
    y
    rz
  Close socket
  Server could be a vision camera
Socket Communication
9
Sample Receive a response
Notes: Sample receive a response

## Slide 105
Socket Communication
9
Available data formats
  String
  Float
  Integer
  Byte
  List
Refer to script manual for full list of socket commands
  Working with set_var() and get_var() allows variable name and integer value to be transmitted in a single message.
Data Formats
Notes: Data formats

## Slide 106
Lab Exercise 1
Socket Communication
9
Write a program to:
  Establish a connection to SocketTest server
  Receive two floats over the socket
  Add them together
  Send the result back to the server.
  Wait for another pair of floats
Example:
  Server sends: (5,2)
  Program returns: 7
Received = (x, y)
Return: Added
Added = x+y
Notes: Socket Communications Lab Exercise

## Slide 107
Socket Communication
9
Write a program to receive simulated vision coordinates over socket, then move to received position:
  Send message to request value over socket then receive three floats
  Move to position, based on pose_trans() example from Variables section.
Data Format:
  Send string “ready” to server
  Read three ascii floats:
  x
  y
  rz
Lab Exercise 2
BASE
Y
X
X
Y
RZ
refpoint
Notes: Ethernet socket Lab Exercise

## Slide 108
Socket Communication
9
Convert your program into a script function:
  The script function must: Connect to the camera (server) over socket Send request message Receive movement parameters from camera Convert the data into a position the robot can move directly into. Return the target position
Use the script function in a program, and call the function to get the target data, and move directly there.
Lab Exercise 3
BASE
Y
X
X
Y
RZ
refpoint
Notes: Ethernet socket Lab Exercise

## Slide 109
1
UR Script
2
Variables
3
Features
4
Advanced use of TCP
5
Modbus Server
6
FTP Server
7
Dashboard Server
8
Client Interfaces
9
Socket Communication
10
Program Troubleshooting
10
Program Troubleshooting

## Slide 110
Program Troubleshooting
10
Log history
  Contains
    Information
    Warnings
    Errors
  Filter with Show/hide
  Retrieve log from robot using Magic file or FTP
Log analysis
  What does messages mean?
  How to improve program structure?
Log file analysis
Notes: Log history
Log history saves valuable information about robot health and program status
History distinguishes between:
» Information
» Warnings
» Errors
Informations, warnings and errors can be hidden/displayed with the buttons above log window top right

## Slide 111
Service
10
Support Log reader
  Read log files
  Convert language
  Export to csv-file
  Filter search
  Supports
    CB3 file format
    CB2 file format
  Refer to Service Manual for error codes and corrective action
Support Log Reader
Notes: Log reader
Demonstrate how use UR Log Reader:
1. Download UR Log Reader from support site
2. Install program and open log_history.txt file

## Slide 112
Program Troubleshooting
10
Errors related to software
Incorrect/Inconvenient program settings in PolyScope
  TCP, Payload, CoG
  Accelerations
  Blends into e.g. Wait
Fix by:
  Correcting program

## Slide 113
Program Troubleshooting
10
Wrong payload, TCP or CoG
The robot compensated for the given payload and CoG offset during movements.
If no payload is given, robot will ”feel” external forces due to the tooling  Protective stops
Higher accelerations amplifies the error, thus causes protective stops more often.

## Slide 114
Program Troubleshooting
10
Blends into stationary position
Robot maintains speed due to blend on Waypoint_2, but next command forces robot to be stationary for 100 ms.
Protective stop due to ”Sudden Stop”

## Slide 115
Program Troubleshooting
10
Motions not ramped down
When IF-statement set to “Check expression continuously”, the robot will stop moving immediately, causing ”Invalid Setpoints: Sudden Stop” error.
Use ”stopj” or ”stopl” to ramp down speed after IF-statement or in ELSE.

## Slide 116
Program Troubleshooting
10
Error code
  Runtime Error: RuntimeError: Infinite loop detected in program
Cause
  If a command is running over and over in a loop without a wait in between
  Program will stop
How to fix
  Add a short WAIT in any loops
  A sync() will also work
Infinite Loop Detected
Notes: Infinite Loop Detected

## Slide 117
Program Troubleshooting
10
Error code
  C154A20: Protective Stop: Position in singularity
Cause
  Singularity problems surface when trying to control robots in Cartesian space (movel / movep).
  A robot singularity occurs when:
    robot axes are redundant (more axes than necessary to cause the same motion) or
    the robot is in certain configurations that require extremely high joint rates to move at some nominal speed in Cartesian space
How to fix
  Use movej() for movements close to singularities
  If movement in Cartesion space is required, adjust waypoints accordingly
  Modify application layout and adjust waypoints accordingly
  Modify end-of-arm tooling by changing angle of the tool direction
Singularities
Notes: Singularities

## Slide 118
Program Troubleshooting
10
Joint Limits
Error code
  C150A20: Protective Stop: Position close to joint limits
Cause
  Indicates that one of the robot joints is at the limit of it’s range
How to fix
  Open the Move tab
  Check the move joint’s section
  If any of the joints are at the end of the range rotate them 360 degrees back to the centre of the range
  Re-teach any MoveJ waypoints
Notes: Joint Limits

## Slide 119
Advanced training
11
You have 30 minutes to answer the questions.
Questions can have multiple answers, so please review all the choices carefully before answering.
Indicate the right answer by ticking or circling the correct choices and filling in the blanks clearly where required.
Feel free to use any material available to you and avoid discussing with other examinees.
Good luck!
Examination
Notes: Examination

## Slide 120
Advanced training
11
1. How do you accommodate for Center of Mass of payload being significantly different from TCP?
  Solution :- Use the script function: set_payload()
2. What are the distance and angle units used in UR scripting?
  Distance : meters Angle : radians
3. What port number is the Dashboard Server available on?
  a. 29999
  b. 30000
  c. 30001
  d. What is the Dashboard Server?
  e. None of the above
4. How would you interface an HMI to the robot?
  a. Use the Dashboard Server on port 29999
  b. Use the secondary client interface on 30002
  c. You cannot bypass the Teach Pendant
  d. (a) or (b)
  e. (b) and (c)
5. The following considerations are important in making a complete risk assessment
  a. Degree of possible harm
  b. Possibility of avoidance
  c. Frequency/duration of exposure
  d. How far the robot is from safety fencing & the number of sensors used
  e. (a)(b) and (c)
Examination Results
Notes: Examination

## Slide 121
Advanced training
11
6. Which URScript command can be used to read the joint positions in radians?
  a. get_actual_tcp_pose()
  b. integer_to_binary_list()
  c. socket_read_ascii_float()
  d. get_actual_joint_positions()
  e. None of the above
7. What does the third value in a pose variable correspond to?
  a. Y rotation
  b. Z rotation
  c. Z position
  d. X position
  e. None of the above
8. What is the reference frame for the pose_add() URScript command?
  a. The first pose argument given
  b. The base frame
  c. The second pose argument given
  d. The photo frame
  e. None of the above
9. When creating a custom feature, the position of origin of the feature frame is at:
  a. The third point in the feature
  b. Halfway between the first and second points
  c. The first point in the feature
  d. The robot base
  e. None of the above
Examination Results
Notes: Examination

## Slide 122
Advanced training
11
10. The difference between an installation variable and a program variable is:
  a. An installation variable contains all the information about where and how the robot is installed, but a program variable does not.
  b. A program variable value is saved between program executions and robot restarts, where as an installation variable is not.
  c. An installation variable value is saved between program executions and robot restarts, where as a program variable is not.
  d. There is no difference.
  e. They are spelt differently.
11. To use the set_tcp() URScript command in a program, you must first:
  a. Set the payload to 0.0kg in the installation tab
  b. Create a new line feature in the installation tab
  c. Set the base feature as variable in the installation tab
  d. Move the robot to the home position
  e. None of the above.
12. The length of a Modbus register is:
  a. 4 bits
  b. 1 byte
  c. 16 bits
  d. 32 bits
  e. None of the above
13. The password you need to use to connect to the robot FTP server is:
  a. Admin
  b. 123456
  c. easybot
  d. terminator
  e. ur
Examination Results
Notes: Examination

## Slide 123
Advanced training
11
14. How many client interfaces are there (not including dashboard server)
  a. 5
  b. 3
  c. 1
  d. 18
  e. 0
15. When using the socket_open() URScript command, when should you use the socket_name parameter?
  a. Always, the command will not work if the socket is not named
  b. When there are multiple sockets opened in a single program
  c. When the port number is higher than 45000
  d. Never
  e. When the socket is feeling lonely
16. What action should be taken to deal with the warning “High Measured Force”
  a. Check TCP/Payload settings
  b. Reduce acceleration parameters in the program
  c. Stop, drop and roll
  d. Reduce the length of the program
  e. (a) and (b)
17. When using socket_read_ascii_float(), the first value in the returned list corresponds to:
  a. The first float sent by the server
  b. The last float sent by the server
  c. The name of the server
  d. The number of floats sent by the server
  e. None of the above
Examination Results
Notes: Examination

## Slide 124
Advanced training
11
18. In a program, if a variable is first assigned an integer value, then later in the program assigned a string value, what will happen?
  a. The program will run without problem, variable types are dynamic
  b. A type error will occur, as a variable already defined as an integer cannot be changed to a string.
  c. A new thread will be created in the program
  d. A second variable will be created containing the string value
  e. The variable will become a Stringteger
19. How can position data be transferred from vision camera to robot?
  a. Using Ethernet socket communication
  b. Using digital I/O’s
  c. Using Modbus registers
  d. All of the above
  e. (a) and (c)
20. Which URscript command(s) is used for calculating the Cartesian distance between two poses?
  a. pose_inv()
  b. get_target_tcp_pose()
  c. pose_sub()
  d. pose_dist()
  e. All of the above
Examination Results
Notes: Examination

## Slide 125
Change log
14
Date | Revision | Initials | Action | Changes
03/06-2016 | 3.3 | PLN | Changed | Slide 112-115
 |  |  | Changed | Screenshots to 3.3 image